## Slide 1
Key points
Endplate bone marrow lesions, which are mainly identified using T1- and T2-weighted MRI (“Modic changes”), are the focus of a large and growing body of work. However, the specific methods for diagnosing these lesions can bias study findings.
The high diagnostic specificity of Modic classification for a painful level contributes to the significant association observed between Modic changes and LBP. Low and variable sensitivity underlies the between- and within-studies variability. Poor sensitivity may be owing to the presence of other pain generators, the limited MRI resolution, and the imperfect reliability of Modic classification.
Magnet strength and pulse sequence parameters can impact the detection of Modic changes.
Advanced pulse sequences may improve reliability and prove valuable for quantifying lesion severity.
Fields AJ, Battié MC, Herzog RJ, Jarvik JG, Krug R, Link TM, Lotz JC, O’Neill CW,
Sharma A; for the ISSLS Degenerative Spinal Phenotypes Group (2019) Measuring and
reporting of vertebral endplate bone marrow lesions as seen on MRI (Modic changes);
recommendations from the ISSLS Degenerative Spinal Phenotypes Group. Eur Spine J;

## Slide 2
SUGGESTED GUIDELINES FOR PRESENTATION OF MODIC CHANGE DATA
MR unit: Identify the MRI instrument and magnetic field strength, plus any surface coils or specialized tables used to collect and amplify signal. Include model number and manufacturer. For longitudinal or multi-center studies, use scanners with the same field strength.
Sequences: Specify the T1- and T2-weighted sequence parameters, including the type of spin echo, repetition time/echo time, field of view, matrix size, slice thickness/spacing, number of echoes, and the type of fat suppression that was applied. If fat suppression was used, the Modic classification for type 2 changes should be defined as having hyperintense signal on T1-weighted images and hypointense on fat-saturated T2-weighted images. If additional sequences will be used for classifying Modic changes, these sequences should be reported in addition to the T1- and T2-weighted sequences.
Image evaluation: Describe which image slices were rated and which levels were evaluated.
Rater agreement: Report the inter-rater and intra-rater kappa statistics for categorical Modic classification. Also, report the inter-rater and intra-rater intraclass correlation coefficients (ICC) if using quantitative measurements.
Fields AJ, Battié MC, Herzog RJ, Jarvik JG, Krug R, Link TM, Lotz JC, O’Neill CW,
Sharma A; for the ISSLS Degenerative Spinal Phenotypes Group (2019) Measuring and
reporting of vertebral endplate bone marrow lesions as seen on MRI (Modic changes);
recommendations from the ISSLS Degenerative Spinal Phenotypes Group. Eur Spine J;

## Slide 3
Take Home Messages
Various methodological factors impact Modic detection and classification.
The lack of standardized reporting guidelines hinders interpretation and comparison of findings between studies.
We believe that development and dissemination of imaging and reporting standards that codify acceptable methodological information is needed, and we recommend that investigators reporting Modic change data follow simple reporting guidelines.
Fields AJ, Battié MC, Herzog RJ, Jarvik JG, Krug R, Link TM, Lotz JC, O’Neill CW,
Sharma A; for the ISSLS Degenerative Spinal Phenotypes Group (2019) Measuring and
reporting of vertebral endplate bone marrow lesions as seen on MRI (Modic changes);
recommendations from the ISSLS Degenerative Spinal Phenotypes Group. Eur Spine J;