## Slide 1
Supplementary Method: CT Protocol and Conditions
All CT images were acquired with a 64-row helical CT system (Optima CT660; GE Healthcare, Chicago, IL, USA). The standard scan parameters were as follows: auto mA of 120 kVp , rotation time of 0.5 s, helical pitch of 0.531, noise index of 3.0, and image noise of SD10. Because minimising the examination time is crucial in post-resuscitation settings, we used reconstructed images aligned to the orbitomeatal (OM) baseline to reduce variations in scanning conditions. For machine learning, we extracted single-slice images at the levels of the foramen of Monro and the pineal gland, which are commonly used in grey-to-white matter ratio (GWR) analysis. Each slice was saved in portable network graphics (PNG) format at a size of 1×256×256, with a window level of 40 Hounsfield units (HU) and window width of 80 HU.