## Slide 1
LipidHunter vs MS-DIAL
Brief summary
One QC sample (positive = 1, negative = 1) of liver samples was used.
MS-DIAL ver.4.9.221218 was used. (the algorithm between v4.2 and 4.9 for annotation is the same.)
LipidHunter(RC2) was used.
The final RANK_SCORE used for filtering annotated lipids in LipidHunter was described below.
・ RANK_SCORE ＞70 PC、PE、TG、DG
・ RANK_SCORE ＞60 PS、PI、PA
・ RANK_SCORE ＞50 PG
If multiple annotations were attached to the same MS2 spectrum in LipidHunter, only the one with the largest RANK_SCORE was adopted.

## Slide 2
MS-DIAL parameter settings

## Slide 3
Lipid Hunter settings
program: LipidHunter(RC2)
[parameters]
vendor = sciex
experiment_mode = LC-MS
lipid_class = PC
charge_mode = [M+CH3COO]-
fawhitelist_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\1-FA_Whitelist_To_MS-DIAL_compair.xlsx
score_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\2-Score_weight_PL.xlsx
mzml_path_str = F:\takahashi\20230209_aging_chk\~liver\02_neg\190618_TT1_Hclass_Aging_029_10_24M_SPF_M_Liver_3_Neg.mzML
img_output_folder_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go
xlsx_output_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\PC_neg.xlsx
rt_start = 1.0
rt_end = 25.0
mz_start = 200.0
mz_end = 1000.0
dda_top = 10
pr_window = 0.75
ms_th = 1000
ms_ppm = 20
ms2_th = 10
ms2_ppm = 50
ms2_infopeak_threshold = 0.001
rank_score_filter = 40.0
score_filter = 40.0
isotope_score_filter = 80.0
lipid_specific_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\3-Specific_ions.xlsx
core_number = 8
max_ram = 48
img_type = png
img_dpi = 300
hunter_folder = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter
hunter_start_time = 2023-03-15_11-53-50
rank_score = True
tag_all_sn = True
fast_isotope = False
ms_max = 0
batch_cfg_file = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\batch\PC.txt
lipid_type = PC
[parameters]
vendor = sciex
experiment_mode = LC-MS
lipid_class = PE
charge_mode = [M-H]-
fawhitelist_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\1-FA_Whitelist_To_MS-DIAL_compair.xlsx
score_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\2-Score_weight_PL.xlsx
mzml_path_str = F:\takahashi\20230209_aging_chk\~liver\02_neg\190618_TT1_Hclass_Aging_029_10_24M_SPF_M_Liver_3_Neg.mzML
img_output_folder_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go
xlsx_output_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\PE_neg.xlsx
rt_start = 1.0
rt_end = 25.0
mz_start = 200.0
mz_end = 1000.0
dda_top = 10
pr_window = 0.75
ms_th = 1000
ms_ppm = 20
ms2_th = 10
ms2_ppm = 50
ms2_infopeak_threshold = 0.001
rank_score_filter = 40.0
score_filter = 40.0
isotope_score_filter = 80.0
lipid_specific_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\3-Specific_ions.xlsx
core_number = 8
max_ram = 48
img_type = png
img_dpi = 300
hunter_folder = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter
hunter_start_time = 2023-03-15_11-59-12
rank_score = True
tag_all_sn = True
fast_isotope = False
ms_max = 0
batch_cfg_file = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\batch\PE.txt
lipid_type = PE

## Slide 4
[parameters]
vendor = sciex
experiment_mode = LC-MS
lipid_class = PG
charge_mode = [M-H]-
fawhitelist_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\1-FA_Whitelist_To_MS-DIAL_compair.xlsx
score_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\2-Score_weight_PL.xlsx
mzml_path_str = F:\takahashi\20230209_aging_chk\~liver\02_neg\190618_TT1_Hclass_Aging_029_10_24M_SPF_M_Liver_3_Neg.mzML
img_output_folder_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go
xlsx_output_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\PG_neg.xlsx
rt_start = 1.0
rt_end = 25.0
mz_start = 200.0
mz_end = 1000.0
dda_top = 10
pr_window = 0.75
ms_th = 1000
ms_ppm = 20
ms2_th = 10
ms2_ppm = 50
ms2_infopeak_threshold = 0.001
rank_score_filter = 40.0
score_filter = 40.0
isotope_score_filter = 80.0
lipid_specific_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\3-Specific_ions.xlsx
core_number = 8
max_ram = 48
img_type = png
img_dpi = 300
hunter_folder = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter
hunter_start_time = 2023-03-15_12-04-05
rank_score = True
tag_all_sn = True
fast_isotope = False
ms_max = 0
batch_cfg_file = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\batch\PG.txt
lipid_type = PG
[parameters]
vendor = sciex
experiment_mode = LC-MS
lipid_class = PS
charge_mode = [M-H]-
fawhitelist_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\1-FA_Whitelist_To_MS-DIAL_compair.xlsx
score_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\2-Score_weight_PL.xlsx
mzml_path_str = F:\takahashi\20230209_aging_chk\~liver\02_neg\190618_TT1_Hclass_Aging_029_10_24M_SPF_M_Liver_3_Neg.mzML
img_output_folder_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go
xlsx_output_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\PS_neg.xlsx
rt_start = 1.0
rt_end = 25.0
mz_start = 200.0
mz_end = 1000.0
dda_top = 10
pr_window = 0.75
ms_th = 1000
ms_ppm = 20
ms2_th = 10
ms2_ppm = 50
ms2_infopeak_threshold = 0.001
rank_score_filter = 40.0
score_filter = 40.0
isotope_score_filter = 80.0
lipid_specific_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\3-Specific_ions.xlsx
core_number = 8
max_ram = 48
img_type = png
img_dpi = 300
hunter_folder = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter
hunter_start_time = 2023-03-15_12-08-08
rank_score = True
tag_all_sn = True
fast_isotope = False
ms_max = 0
batch_cfg_file = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\batch\PS.txt
lipid_type = PS

## Slide 5
[parameters]
vendor = sciex
experiment_mode = LC-MS
lipid_class = PA
charge_mode = [M-H]-
fawhitelist_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\1-FA_Whitelist_To_MS-DIAL_compair.xlsx
score_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\2-Score_weight_PL.xlsx
mzml_path_str = F:\takahashi\20230209_aging_chk\~liver\02_neg\190618_TT1_Hclass_Aging_029_10_24M_SPF_M_Liver_3_Neg.mzML
img_output_folder_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go
xlsx_output_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\PA_neg.xlsx
rt_start = 1.0
rt_end = 25.0
mz_start = 200.0
mz_end = 1000.0
dda_top = 10
pr_window = 0.75
ms_th = 1000
ms_ppm = 20
ms2_th = 10
ms2_ppm = 50
ms2_infopeak_threshold = 0.001
rank_score_filter = 40.0
score_filter = 40.0
isotope_score_filter = 80.0
lipid_specific_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\3-Specific_ions.xlsx
core_number = 8
max_ram = 48
img_type = png
img_dpi = 300
hunter_folder = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter
hunter_start_time = 2023-03-15_11-51-25
rank_score = True
tag_all_sn = True
fast_isotope = False
ms_max = 0
batch_cfg_file = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\batch\PA.txt
lipid_type = PA
[parameters]
vendor = sciex
experiment_mode = LC-MS
lipid_class = PI
charge_mode = [M-H]-
fawhitelist_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\1-FA_Whitelist_To_MS-DIAL_compair.xlsx
score_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\2-Score_weight_PL.xlsx
mzml_path_str = F:\takahashi\20230209_aging_chk\~liver\02_neg\190618_TT1_Hclass_Aging_029_10_24M_SPF_M_Liver_3_Neg.mzML
img_output_folder_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go
xlsx_output_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\PI_neg.xlsx
rt_start = 1.0
rt_end = 25.0
mz_start = 200.0
mz_end = 1000.0
dda_top = 10
pr_window = 0.75
ms_th = 1000
ms_ppm = 20
ms2_th = 10
ms2_ppm = 50
ms2_infopeak_threshold = 0.001
rank_score_filter = 40.0
score_filter = 40.0
isotope_score_filter = 80.0
lipid_specific_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\3-Specific_ions.xlsx
core_number = 8
max_ram = 48
img_type = png
img_dpi = 300
hunter_folder = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter
hunter_start_time = 2023-03-15_12-06-12
rank_score = True
tag_all_sn = True
fast_isotope = False
ms_max = 0
batch_cfg_file = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\batch\PI.txt
lipid_type = PI

## Slide 6
[parameters]
vendor = sciex
experiment_mode = LC-MS
lipid_class = TG
charge_mode = [M+NH4]+
fawhitelist_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\1-FA_Whitelist_To_MS-DIAL_compair.xlsx
score_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\2-Score_weight_TG.xlsx
mzml_path_str = F:\takahashi\20230209_aging_chk\~liver\01_pos\190618_TT1_Hclass_Aging_029_10_24M_SPF_M_Liver_3_Pos.mzML
img_output_folder_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go
xlsx_output_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\TG_NH4.xlsx
rt_start = 1.0
rt_end = 30.0
mz_start = 200.0
mz_end = 1200.0
dda_top = 10
pr_window = 0.75
ms_th = 1000
ms_ppm = 20
ms2_th = 10
ms2_ppm = 50
ms2_infopeak_threshold = 0.001
rank_score_filter = 50.0
score_filter = 50.0
isotope_score_filter = 80.0
lipid_specific_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\3-Specific_ions.xlsx
core_number = 8
max_ram = 64
img_type = png
img_dpi = 300
hunter_folder = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter
hunter_start_time = 2023-03-15_15-22-06
rank_score = True
tag_all_sn = True
fast_isotope = False
ms_max = 0
batch_cfg_file = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\batch\TG_NH4.txt
lipid_type = TG
[parameters]
vendor = sciex
experiment_mode = LC-MS
lipid_class = DG
charge_mode = [M+NH4]+
fawhitelist_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\1-FA_Whitelist_To_MS-DIAL_compair.xlsx
score_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\2-Score_weight_DG.xlsx
mzml_path_str = F:\takahashi\20230209_aging_chk\~liver\01_pos\190618_TT1_Hclass_Aging_029_10_24M_SPF_M_Liver_3_Pos.mzML
img_output_folder_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go
xlsx_output_path_str = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\DG_NH4.xlsx
rt_start = 1.0
rt_end = 20.0
mz_start = 200.0
mz_end = 1000.0
dda_top = 10
pr_window = 0.75
ms_th = 1000
ms_ppm = 20
ms2_th = 10
ms2_ppm = 50
ms2_infopeak_threshold = 0.001
rank_score_filter = 40.0
score_filter = 40.0
isotope_score_filter = 80.0
lipid_specific_cfg = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter\ConfigurationFiles\3-Specific_ions.xlsx
core_number = 8
max_ram = 48
img_type = png
img_dpi = 300
hunter_folder = F:\takahashi\20230209_aging_chk\Lipidhunter\LipidHunter2_RC\LipidHunter
hunter_start_time = 2023-03-15_11-36-59
rank_score = True
tag_all_sn = True
fast_isotope = False
ms_max = 0
batch_cfg_file = F:\takahashi\20230209_aging_chk\Lipidhunter\20230315_Go\batch\DG_NH4.txt
lipid_type = DG

## Slide 7
onlyMsDial | both |  | onlyLipidHunter
PC 16:0_17:1 | PC 15:0_16:0 | PC 16:0_20:4 | PC 14:0_18:2
PC 16:0_20:5 | PC 16:0_16:0 | PC 16:1_20:4 | PC 18:1_18:1
PC 18:0_20:2 | PC 16:0_16:1 | PC 19:0_18:2 | PC 18:2_18:2
PC 19:1_20:4 | PC 16:1_16:1 | PC 17:0_20:3 | PC 18:2_18:3
PC 18:0_22:4 | PC 15:0_18:2 | PC 17:0_20:4 | PC 15:0_22:6
PC 20:0_20:4 | PC 16:0_18:0 | PC 17:1_20:4 | PC 18:1_20:3
PC 19:0_22:6 | PC 16:0_18:1 | PC 18:0_20:3 | PC 18:3_20:4
PC 20:4_22:6 | PC 16:0_18:2 | PC 18:0_20:4 | PC 20:4_20:4
PC 20:1_22:6 | PC 16:0_18:3 | PC 18:1_20:4 | 
 | PC 16:1_18:2 | PC 16:0_22:6 | 
 | PC 17:0_18:1 | PC 18:2_20:4 | 
 | PC 17:0_18:2 | PC 16:1_22:6 | 
 | PC 17:1_18:2 | PC 19:0_20:4 | 
 | PC 15:0_20:4 | PC 17:0_22:6 | 
 | PC 18:0_18:1 | PC 17:1_22:6 | 
 | PC 18:0_18:2 | PC 18:0_22:5 | 
 | PC 16:0_20:3 | PC 18:0_22:6 | 
 | PC 18:1_18:2 | PC 18:1_22:6 | 

## Slide 8
only in MS-DIAL | both |  | only in LipidHunter
PE 16:0_16:1 | PE 16:0_18:1 | PE 15:0_22:6 | PE 16:0_18:3
PE 16:0_17:1 | PE 16:0_18:2 | PE 18:0_20:3 | PE 16:0_20:3
PE 17:0_18:1 | PE 16:1_18:2 | PE 18:0_20:4 | PE 16:0_20:5
PE 17:1_18:2 | PE 17:0_18:2 | PE 18:1_20:4 | PE 18:1_18:1
PE 18:0_20:1 | PE 15:0_20:4 | PE 16:1_22:6 | PE 18:2_22:6
PE 18:0_20:2 | PE 18:0_18:1 | PE 19:0_20:4 | 
PE 20:0_20:4 | PE 18:0_18:2 | PE 17:0_22:6 | 
PE 19:0_22:6 | PE 18:1_18:2 | PE 17:1_22:6 | 
PE 20:1_22:6 | PE 16:0_20:4 | PE 18:0_22:4 | 
 | PE 18:2_18:2 | PE 18:0_22:5 | 
 | PE 16:1_20:4 | PE 18:0_22:6 | 
 | PE 17:0_20:4 | PE 18:1_22:6 | 
 | PE 17:1_20:4 |  | 

## Slide 9
only in MS-DIAL | both | only in LipidHunter
PG 16:0_16:1 | PG 16:0_18:1 | PG 18:1_18:3
PG 16:1_18:2 | PG 16:0_18:2 | 
PG 16:0_20:4 | PG 16:1_18:1 | 
PG 18:2_18:3 | PG 18:0_18:2 | 
PG 18:1_20:3 | PG 18:1_18:1 | 
PG 18:2_20:4 | PG 18:1_18:2 | 
PG 17:1_22:6 | PG 18:2_18:2 | 
PG 18:3_22:6 | PG 18:1_20:4 | 
PG 23:0_18:1 | PG 16:1_22:6 | 
PG 20:3_22:6 | PG 18:1_22:5 | 
 | PG 18:1_22:6 | 
 | PG 18:2_22:6 | 
 | PG 20:4_22:6 | 
 | PG 22:5_22:6 | 
 | PG 22:6_22:6 | 

## Slide 10
only in MS-DIAL | both | only in LipidHunter
PI 16:1_18:2 | PI 17:0_18:2 | PI 16:0_18:2
PI 17:1_18:2 | PI 18:0_18:2 | 
PI 18:0_18:1 | PI 16:0_20:4 | 
PI 16:1_20:4 | PI 17:0_20:4 | 
PI 19:1_20:4 | PI 18:0_20:3 | 
PI 17:0_22:6 | PI 18:1_20:4 | 
PI 18:0_22:4 | PI 16:0_22:6 | 
PI 18:0_22:5 | PI 19:0_20:4 | 
PI 18:1_22:6 | PI 18:0_22:6 | 

## Slide 11
only in MS-DIAL | both | only in LipidHunter
PS 19:0_20:4 | PS 18:0_18:1 | PS 15:0_18:0
 | PS 16:0_20:4 | PS 17:0_18:0
 | PS 17:0_20:4 | PS 18:0_18:2
 | PS 18:1_20:4 | PS 18:0_18:0
 | PS 16:0_22:6 | 
 | PS 17:0_22:6 | 
 | PS 18:0_22:5 | 
 | PS 18:0_22:6 | 

## Slide 12
only in MS-DIAL | both | only in LipidHunter
PA 16:0_18:1 |  | PA 18:1_20:2
PA 16:0_18:2 |  | PA 22:6_22:6
PA 16:0_20:4 |  | 

## Slide 13
only in MS-DIAL | both |  | only in LipidHunter
TG 8:0_8:0_8:0 | TG 8:0_16:0_22:6 | TG 15:0_16:1_18:1 | TG 14:0_16:1_16:1
TG 8:0_8:0_10:0 | TG 8:0_16:0_18:2 | TG 18:1_18:2_18:2 | TG 15:0_18:1_18:1
TG 8:0_16:1_16:1 | TG 9:0_16:0_18:2 | TG 15:0_18:1_18:2 | TG 16:0_12:1_18:2
TG 9:0_16:1_18:2 | TG 8:0_16:0_18:1 | TG 16:0_18:1_22:6 | TG 16:0_16:1_18:3
TG 8:0_16:0_16:1 | TG 10:0_16:0_18:2 | TG 17:1_18:1_18:2 | TG 16:0_18:0_20:1
TG 8:0_16:0_20:4 | TG 16:1_18:2_18:4 | TG 18:1_18:1_22:6 | TG 16:0_18:2_18:2
TG 8:0_17:0_16:1 | TG 14:1_16:1_18:2 | TG 14:0_16:0_16:0 | TG 16:0_18:2_18:3
TG 9:0_16:0_20:4 | TG 16:1_16:1_18:3 | TG 14:0_16:0_18:1 | TG 16:0_18:2_18:4
TG 9:0_18:1_18:2 | TG 18:2_18:3_22:6 | TG 16:0_16:1_18:1 | TG 16:0_20:4_22:6
TG 10:0_16:0_20:4 | TG 10:0_16:0_18:1 | TG 16:0_18:1_18:2 | TG 16:1_16:1_16:1
TG 12:0_16:1_18:2 | TG 15:0_16:1_18:3 | TG 18:1_18:1_22:5 | TG 16:1_18:2_20:5
TG 9:0_16:0_18:1 | TG 16:1_18:2_18:3 | TG 18:1_18:1_18:2 | TG 17:0_18:1_20:4
TG 11:0_16:0_18:2 | TG 16:1_18:2_22:6 | TG 15:0_16:0_18:1 | TG 17:0_18:1_22:5
TG 14:1_16:1_17:1 | TG 14:0_16:1_18:2 | TG 18:1_18:1_20:3 | TG 17:0_18:1_22:6
TG 14:0_18:2_22:6 | TG 15:0_18:2_18:3 | TG 16:0_16:0_16:0 | TG 17:1_18:1_18:1
TG 16:0_14:1_16:1 | TG 16:1_16:1_18:2 | TG 16:0_16:0_18:1 | TG 17:1_18:1_20:4
TG 14:0_15:0_16:1 | TG 18:2_18:2_22:6 | TG 18:1_18:1_22:4 | TG 18:0_18:1_18:1
TG 18:1_22:6_22:6 | TG 18:2_18:2_18:3 | TG 16:0_18:1_18:1 | TG 18:0_18:1_20:1
TG 14:0_14:0_16:0 | TG 15:0_18:2_22:6 | TG 18:1_18:1_18:1 | TG 18:1_18:1_20:4
TG 17:1_18:2_18:2 | TG 18:2_20:4_22:6 | TG 18:1_20:1_18:2 | TG 18:1_18:2_19:2
TG 14:0_15:0_16:0 | TG 16:1_18:2_18:2 | TG 16:0_16:0_17:0 | TG 18:1_18:2_20:4
TG 17:1_19:2_19:3 | TG 17:1_18:2_22:6 | TG 16:0_17:0_18:1 | TG 18:1_18:2_22:5
TG 18:1_18:1_19:3 | TG 15:0_16:1_18:2 | TG 17:0_18:1_18:1 | TG 18:1_18:2_24:6
TG 15:0_16:0_16:0 | TG 14:0_16:0_16:1 | TG 18:1_18:1_19:1 | TG 18:1_18:5_21:5
TG 18:1_18:1_24:6 | TG 18:1_18:2_18:3 | TG 18:1_18:1_22:3 | TG 18:2_18:2_18:2
TG 16:0_17:1_18:1 | TG 15:0_18:2_18:2 | TG 16:0_16:0_18:0 | TG 18:2_18:2_20:4
TG 17:0_18:1_18:2 | TG 18:1_20:4_22:6 | TG 16:0_18:0_18:1 | TG 18:2_18:3_18:3
TG 18:1_19:1_18:2 | TG 16:0_16:1_16:1 | TG 18:1_18:1_20:1 | TG 19:0_18:1_18:1
TG 18:1_18:1_24:4 | TG 16:0_18:2_22:6 | TG 18:1_22:1_18:2 | TG 7:0_16:0_18:1
TG 16:0_18:1_20:1 | TG 18:1_18:2_22:6 | TG 17:0_18:0_18:1 | TG 7:0_16:0_18:2
TG 18:1_18:1_22:1 | TG 16:0_16:1_18:2 | TG 17:0_18:1_20:1 | 
TG 18:0_18:0_18:0 | TG 15:0_18:1_22:6 | TG 16:0_18:0_18:0 | 
 | TG 16:1_18:1_18:2 | TG 16:0_20:0_18:1 | 
 | TG 17:1_18:1_22:6 | TG 16:0_18:1_22:1 | 
 | TG 15:0_16:0_16:1 |  | 

## Slide 14
only in MS-DIAL | both | only in LipidHunter
DG 16:1_22:6 | DG 16:1_18:2 | DG 14:0_18:1
DG 16:1_16:1 | DG 18:2_18:2 | DG 16:1_18:1
DG 18:2_20:4 | DG 16:0_16:1 | DG 18:1_18:3
DG 15:0_18:2 | DG 16:0_22:6 | DG 18:2_38:8
DG 14:0_16:0 | DG 16:0_20:4 | 
DG 18:1_22:6 | DG 16:0_18:2 | 
DG 15:0_18:1 | DG 18:1_18:1 | 
DG 17:0_20:4 | DG 18:1_20:4 | 
DG 17:0_18:2 | DG 18:1_18:2 | 
DG 18:0_22:6 | DG 16:0_16:0 | 
DG 18:0_20:3 | DG 16:0_18:1 | 
 | DG 18:0_20:4 | 
 | DG 17:0_18:1 | 
 | DG 16:0_18:0 | 
 | DG 18:0_18:1 | 
 | DG 18:1_20:1 | 

## Slide 15
LipidMatch vs MS-DIAL
Brief summary
Seven QC samples (positive = 7, negative = 7) of liver samples were used.
MS-DIAL ver.4.9.221218 was used.
LipidMatch3.0.0 was used.

## Slide 16
MS-DIAL parameter settings

## Slide 17
LIPIDMATCH_PARAMETERS_SciEx.csv
Parameters,Values,Notes
RT Window (for matching peaks to MS/MS scans),0.14,0.14 would be RT plus or minus 0.07 minute search window (can be seconds as well if that is what units are in)
MZ Search Tolerance MS1 (Da),0.016,0.005 would be MZ plus or minus 0.005 Da search window
MZ Search Window MS2 (ppm),20,10 would be MZ plus or minus 5 ppm search window
Isolation Window (selection accuracy),1,amu or Da. 1 would be MZ plus or minus 0.5
Minimum Scans for Fragment,1,Minimum number of scan with a fragment observed for that fragment to be considered real
Intensity Threshold MS2,15,Necessary for a fragment mass to be considered real
AIF minimum number of scans,NA,Minimum number of scan with a fragment observed for that fragment to be considered real
AIF correlation cutoff,NA,Adjusted R2 correlation between precursors and fragments
Comments Column (row ID. Should be numeric,1,Must be changed to match your data format
MZ Column (in feature table),3,Must be changed to match your data format
RT Column (in feature table),2,Must be changed to match your data format
row numeric data starts (in feature table),6,Must be changed to match your data format
Directory of Inputs,C:/Users/mikikot/Desktop/LipidMatch/liver/MS2neg/,"Directory (Must be changed) (use forward slash ""/"", end in ""/"")“
Directory of Libraries,C:/Users/mikikot/Desktop/LipidMatch/LipidMatch-3.0.0/LipidMatch_Libraries_Acetate/,"Directory (Must be changed) (use forward slash ""/"", end in ""/"")"
LipidMatch parameter settings
The annotation rank “1” and “3” were used as the annotated lipid molecules where the numbers of 1 and 3 denote for molecular species level and species level annotations, respectively.

## Slide 18
Annotated peak number
MS-DIAL vs LipidMatch (see the detail at vs_LipidMatch_dataset_VS2.xlsx)
4489 peaks are MS2 measured
Name Unmatched
3526 peaks are MS2 measured
Name Unmatched