## Slide 1
100 ng to 3 ug Starting DNA
Incoming DNA Quantification via Picogreen
DNA Shearing & With-Bead Cleanup (3.0x )
End Repair &
With-Bead Cleanup (2.2x)
Volume Check
Fragment Size Analysis Caliper GX
A Base Addition & With-Bead Cleanup (2.2x)
✔
✔
✔
✔
Quality Control Checkpoint





Adapter Ligation & With-Bead Cleanup (0.7x)
Pond PCR & With-Bead Cleanup (1.8x)
Normalization of all samples to
25 ng/ul
Fragment Size Analysis Caliper GX
Picogreen Quantification
✔





Hybridization of Pond & Bait
72 hours
Picogreen Quantification & Normalization
Capture & Wash
on
Streptavidin Beads
Direct PCR off bead & With-Bead Cleanup (1.8x)
qPCR to determine optimal cluster density
✔




✔
✔


Solution Hybrid Selection Process Map
Cluster Amplification
Check Fingerprint Panel for Concordance
Sequencing
Measure Performance (Metrics)
✔



✔
