## Slide 1: Hemodialysis Safety Checklist
Sign In
Have you copied any new or unsigned orders since last treatment?
_______________________________
Is the dialysate set up in agreement with the ordered dialysate as documented on the kardex?
Is the anticoagulation type and dose set up on the machine as per the ordered anticoagulation on the kardex?
_______________________________
Are there laboratory tests ordered for today?
Do you have the correct labels, tubes and requisitions?
_______________________________
Are there any meds due to be administered pre, intra, or post dialysis according to the MAR?
Sign Out
VASCULAR ACCESS review:
Has mupirocin been applied to buttonholes?
Has CVC dressing been changed?
Over 2 needling attempts to AVF/AVG reported to VAC?
Signs of infection? Report to VAC/NP/MD
___________________________________
Record patient BP
Record patient weight
___________________________________
Does patient meet discharge criteria?
Time Out
Verify the following dialysis prescription with the patient:
  TIME
  BATH (Na, K, calcium and glucose)
  ANTICOAGULATION type
  TARGET WEIGHT
  SODIUM/FLUID RAMP
Confirm UNIQUE ORDERS have been followed such as non-routine dialyzer (Toray), extra N/S rinse, dual dialyzer
_____________________________________
Review LABWORK to be taken pre and post dialysis
Verify MEDICATIONS to be given
_____________________________________
Confirm with patient VASCULAR ACCESS needs – needle gauge, U/S guidance for cannulation, line reversal for CVC
INSPECT access – any signs of infection?
Is ACCESS FLOW due?
_____________________________________
Wash hands
“Is there anything else we should be thinking about before we start your dialysis?”
Before patient enters unit Before Initiation Before patient leaves unit